## Slide 1
Introducing New Products

## Slide 2
T-Bar 50W LED Panel
Features:
Samsung LED chip
Lifespan: 50,000 hours
CCT: 5700K
Dimmable: Yes (0-10V, PWM, R)
Product Description:
+ Equipped with a 0-10V dimmable constant-current driver and an advanced optical diffuser, aluminum alloy frame, ensuring good lighting uniformity and high efficiency.
+ With built-in driver, it can be mounted directly to junction boxes.
+ Able to be operated within a wide range input voltage of AC 100-277V.
+ Able to control the brightness with a 0-10V dimmer or step-dimming driver.
With slim and elegant shape, this LED panel light is suitable for both residential and commercial sectors, replacing existing fluorescent troffer light fixtures.
Quality:
In compliance with UL/DLC regulations
Size | Lumen | Efficacy | Weight | Illumination-equivalent
L1200xW300mm | 5500lm | 110lm/W | 4.9 kg | 2x32W FL T8
L600xW600mm | 5500lm | 110lm/W | 4.9 kg | 4x18W FL T8
Specifications:

## Slide 3
T-Bar 50W LED Panel (Tunable White)
Features:
Samsung LED chip
Lifespan: 50,000 hours
CCT-Tunable: 3000/ 5700/ 6500K
Dimmable and CCT-changeable by Wifi or Bluetooth
Product Description:
+ Color temperature can be adjusted from 3000K to 5000K with the tunable white controller (to be sold separately).
+ Able to dim the light and change color temperature with just 1 simple touch on smartphone.
+ The 2 by 4 bi-color LED light is designed for suspended grid ceilings or can be used with a hanging kit.
+ With advanced technology and an optical diffuser, it delivers a smooth, flawless wall of illumination without visible bulbs or hot spots.
+ Its light emits up to 4,500 lumens of illumination—equivalent to the output of 4 18-watt fluorescent T8 tubes and operates within a wide input voltage range of 100-277 VAC, has a sturdy aluminum alloy frame with a white finish, and lasts 5 times longer than fluorescent lights.
This tunable-white LED Panel light is perfect for photography sector, continuous lighting, office, school, hospital lighting, gymnasium, basement, and other applications where it's beneficial to mimic natural daylight cycles.
Size | Lumen | Efficacy | Weight | Illumination-equivalent
L1212xW300mm | 4500lm | 90lm/W | 4.9kg | 2x32W FL T8
L600xW600mm | 4500lm | 90lm/W | 4.9kg | 4x18W FL T8
Specifications:
6500K
5700K
3000K

## Slide 4
T-Bar LED Panel (Ambient Light Sensor)
Product Description:
The luminaire lights on 100% illumination or dims to maintain the preset illumination level against ambient light.
Save at least 30%
of total energy
Specifications:
No. | Size | Wattage | Voltage | Frequency | PF | Lumen | Luminous Efficacy | CRI | CCT | Lifetime | Dimmable
1 | L600×W600mm | 50W | 220V | 60Hz | 0.9 | 5500lm | 110lm/W | 80 | 5700K | 25,000hrs | Yes
2 | L1200×W300mm | 50W | 220V | 60Hz | 0.9 | 5500lm | 110lm/W | 80 | 5700K | 25,000hrs | Yes
Sensor

## Slide 5
M-Bar LED Panel
Product Description
Rang Dong’s LED Panel light is equipped with Samsung 4014 luminous source, providing excellent lumen output, long-lasting stability and splendid sight.
No. | Size | Wattage | Voltage | Frequency | PF | Lumen | Luminous Efficacy | CRI | CCT | Lifetime
1 | L320xW320mm | 15W | 220V | 60Hz | 0.9 | 1200lm | 80lm/W | 80 | 5700K | 25,000hrs
2 | L640×W320mm | 25W | 220V | 60Hz | 0.9 | 2250lm | 90lm/W | 80 | 5700K | 25,000hrs
3 | L640xW180mm | 25W | 220V | 60Hz | 0.9 | 2250lm | 90lm/W | 80 | 5700K | 25,000hrs
4 | L950xW180mm | 30W | 220V | 60Hz | 0.9 | 2700lm | 90lm/W | 80 | 5700K | 25,000hrs
5 | L750xW320mm | 30W | 220V | 60Hz | 0.9 | 2700lm | 90lm/W | 80 | 5700K | 25,000hrs
6 | L1280xW180mm | 40W | 220V | 60Hz | 0.9 | 4400lm | 110lm/W | 80 | 5700K | 25,000hrs
7 | L520xW520mm | 40W | 220V | 60Hz | 0.9 | 4400lm | 110lm/W | 80 | 5700K | 25,000hrs
8 | L640×W640mm | 50W | 220V | 60Hz | 0.9 | 5500lm | 110lm/W | 80 | 5700K | 25,000hrs
9 | L1280×W320mm | 50W | 220V | 60Hz | 0.9 | 5500lm | 110lm/W | 80 | 5700K | 25,000hrs
Specifications:
5700K (80 CRI)
Low power consumption, saving more than 50%
of energy compared to existing fluorescent luminaire

## Slide 6
M-Bar LED Panel (CCT-changeable by Switch)
CCT Switch
ON
OFF
3000K
4000K
6500K
Specifications:
Features:
No. | Size | Wattage | Voltage | Frequency | PF | Lumen | Luminous Efficacy | CRI | CCT | Lifetime
1 | L320xW320mm | 15W | 220V | 60Hz | 0.9 | 1200lm | 80lm/W | 80 | 3000/4000/6500K | 25,000hrs
2 | L640×W320mm | 25W | 220V | 60Hz | 0.9 | 2250lm | 90lm/W | 80 | 3000/4000/6500K | 25,000hrs
3 | L640xW180mm | 25W | 220V | 60Hz | 0.9 | 2250lm | 90lm/W | 80 | 3000/4000/6500K | 25,000hrs
4 | L950xW180mm | 30W | 220V | 60Hz | 0.9 | 2700lm | 90lm/W | 80 | 3000/4000/6500K | 25,000hrs
5 | L750xW320mm | 30W | 220V | 60Hz | 0.9 | 2700lm | 90lm/W | 80 | 3000/4000/6500K | 25,000hrs
6 | L1280xW180mm | 40W | 220V | 60Hz | 0.9 | 3600lm | 90lm/W | 80 | 3000/4000/6500K | 25,000hrs
7 | L520xW520mm | 40W | 220V | 60Hz | 0.9 | 3600lm | 90lm/W | 80 | 3000/4000/6500K | 25,000hrs
8 | L640×W640mm | 50W | 220V | 60Hz | 0.9 | 4500lm | 90lm/W | 80 | 3000/4000/6500K | 25,000hrs
9 | L1280×W320mm | 50W | 220V | 60Hz | 0.9 | 4500lm | 90lm/W | 80 | 3000/4000/6500K | 25,000hrs

## Slide 7
LED Panel M-Bar (3-Step Dimming by Switch)
Applications:
Specifications:
When nature light is sufficient
34%
When it is dark outside
100%
When using the projector in a meeting
8%
Save at least 30% of total energy
CCT Switch
ON
OFF
No. | Size | Wattage | Voltage | Frequency | PF | Lumens | Luminous Efficacy | CRI | CCT | Lifetime
1 | L320xW320mm | 15W | 220V | 60Hz | 0.9 | 1200lm | 80lm/W | 80 | 5700K | 25,000hrs
2 | L640xW320mm | 25W | 220V | 60Hz | 0.9 | 2250lm | 90lm/W | 80 | 5700K | 25,000hrs
3 | L640xW180mm | 25W | 220V | 60Hz | 0.9 | 2250lm | 90lm/W | 80 | 5700K | 25,000hrs
4 | L950xW180mm | 30W | 220V | 60Hz | 0.9 | 2700lm | 90lm/W | 80 | 5700K | 25,000hrs
5 | L750xW320mm | 30W | 220V | 60Hz | 0.9 | 2700lm | 90lm/W | 80 | 5700K | 25,000hrs
6 | L1280xW180mm | 40W | 220V | 60Hz | 0.9 | 3600lm | 90lm/W | 80 | 5700K | 25,000hrs
7 | L520xW520mm | 40W | 220V | 60Hz | 0.9 | 3600lm | 90lm/W | 80 | 5700K | 25,000hrs
8 | L640xW640mm | 50W | 220V | 60Hz | 0.9 | 4500lm | 90lm/W | 80 | 5700K | 25,000hrs
9 | L1280xW320mm | 50W | 220V | 60Hz | 0.9 | 4500lm | 90lm/W | 80 | 5700K | 25,000hrs

## Slide 8
Specifications:
Driver type | Power (W) | Type | Size (Φ*H) mm | Voltage/ Frequency | PF | Lumen (lm) | Luminous Efficacy | CCT (K) | Housing material | Beam angle | LED chip | Certification | Lifetime (hrs) | Unit price (USD)
Linear IC | 15W | 6 inches | 180×74 | 220V/60Hz | 0.5 | 1500 | 100 | 3000/ 5700/ 6500 | ADC12 | 110° | Samsung/ SCC | EMC | 20,000 | 
Linear IC | 20W | 6 inches | 180×74 | 220V/60Hz | 0.5 | 2000 | 100 |  | ADC12 | 110° | Samsung/ SCC | EMC | 20,000 | 
Buck | 15W | 6 inches | 180×74 | 220V/60Hz | 0.9 | 1500 | 100 |  | ADC12 | 110° | Samsung/ SCC | EMC | 25,000 | 
Buck | 20W | 8 inches | 242×94 | 220V/60Hz | 0.9 | 2000 | 100 |  | ADC12 | 110° | Samsung/ SCC | EMC | 25,000 | 
50%
LED Downlight
 | LED Downlight | CFC Downlight
Energy used | 15W | 30W
Energy used | 20W | 40W
Energy used | 30W | 60W
Warranty | 2 years | 1 year
Product Description
A luminaire that is well recognized in the global market for its unconventional design and outstanding performance. Its special features include ease of installation, reliable quality and high efficiency. This product can be used in many application areas including office, education, residence, hospital, etc.
Our LED Downlight was designed with the consideration of both a long lifespan and high light efficacy, while taking into account user's productivity, safety and health.

## Slide 9
Specifications:
Driver type | Power (W) | Size (ΦxH) mm | Voltage/ Frequency | PF | Lumen (lm) | Luminous Efficacy (lm/W) | CCT (K) | Housing material | Beam angle | LED chip | Certification | Lifetime | Unit price
Linear IC | 15 | 175×35 | 220V/60Hz | 0.5 | 1500 | 100 | 3000K 5700K 6500K | Steel | 110° | Samsung/ SSC | EMC | 20,000hrs | 
Linear IC | 20 | 175×35 | 220V/60Hz | 0.5 | 2000 | 100 |  | Steel | 110° | Samsung/ SSC | EMC | 20,000hrs | 
Buck | 15 | 175×65 | 220V/60Hz | 0.9 | 1500 | 100 |  | Steel | 110° | Samsung/ SSC | KC Cert | 25,000hrs | 
Buck | 20 | 175×65 | 220V/60Hz | 0.9 | 2000 | 100 |  | Steel | 110° | Samsung/ SSC | KC Cert | 25,000hrs | 
LED Downlight
 | LED Downlight | CFC Downlight
Energy used | 15W | 30W
Energy used | 20W | 40W
Warranty | 2 years | 1 year
50%

## Slide 10
Specifications:
Driver Type | Wattage (W) | Type | Size (LxWxH) mm | Voltage/ Frequency | PF | Lumen (lm) | Luminous Efficacy (lm/W) | CCT (K) | Housing material | Beam angle | LED chip | Certification | Lifetime | Unit price (USD)
IC Linear | 30 | Linear | 600x60x50 | 220V/60Hz | 0.5 | 2300 | 76 | 3000 5700 6500 | PC | 120° | Samsung/ SSC | EMC | 30,000hrs | 
IC Linear | 50 | Cross | 600x600x50 | 220V/60Hz | 0.5 | 4300 | 86 |  | PC | 120° | Samsung/SSC | EMC | 20,000hrs | 
LED Linear/Cross light
Features:
Low power consumption, saving more than 50% of energy compared to existing fluorescent luminaires.
Uniform spread of light.
Easy to install and maintain.
Applications:
Replaces exposed / fixed fixture installed fluorescent lamp and interior lamp
Residential, parking lot, subway and commercial and industrial structures.

## Slide 11
Specifications:
Driver Type | Wattage (W) | Size (LxWxH) mm | Voltage/ Frequency | PF | Lumen (lm) | Luminous Efficacy (lm/W) | CCT (K) | Housing material | Beam angle | LED chip | Certification | Lifetime (hrs) | Unit price (USD)
Buck | 36 | 1200x75x24 | 220V/60Hz | 0.9 | 3400 | 95 | 3000/ 6500 | Al+PC | 120° | Samsung/ SSC | EMC | 15,000 | 
LED Linear/Cross light
Features:
Low power consumption saves more than 50% of energy compared to existing fluorescent luminaires
Various size (300/600/900/1200mm)
Slim and simple design
Uniform spread of light.
Easy to install and maintain.
Applications:
Apartment entrance, hallway lighting, indoor lighting
Parking lot, subway, commercial, industrial, etc. lighting
M16L 120/36W

## Slide 12
Specifications:
LED Linear/Cross light
Features:
This product with IP65 ingress protection degree suitables for dry, damp and wet locations
Low power consumption, saving more than 50% of energy compared to existing fluorescent luminaires.
Uniform spread of light.
Easy to install and maintain.
Applications:
Parking lot, subway, commercial lighting
Apartment entrance, hallway lighting, indoor lighting
Warehouse, factory, gymnasium, etc. lighting
Driver Type | Wattage (W) | Size (LxWxH) mm | Voltage/ Frequency | PF | Lumen (lm) | Luminous Efficacy (lm/W) | CCT (K) | Housing material | Beam angle | LED chip | Certification | Lifetime (hrs) | Unit price (USD)
Buck | 36 | 1200x80x78 | 220V/60Hz | 0.5 | 3420 | 95 | 3000/ 6500 | Al+PC | 120° | Samsung/ SSC | EMC | 15,000 | 
M18L 120/36W

## Slide 13
20W Hybrid LED Tube (Full Glass)
Product Description
Hybrid LED Tube is made of glass, which does not bend and is non-flammable, and powder coated to ensure good heat transfer. This Hybrid LED Tube can replace any existing T8 fluorescent tube and is compatible with AC 220V/60Hz. The tube can be installed using the existing ballast or bypass mode.
Features:
Samsung LED chip
Lifespan: 50,000 hours
CCT: 5700K
Energy efficient design
Cost-saving
Mercury and Lead Free
Specifications:
Installation:
Driver Type | Wattage (W) | Voltage/ Frequency | PF | Lumen (lm) | Luminous Efficacy (lm/W) | CCT (K) | Beam angle | LED chip | Certification | Base Cap | Lifetime (hrs) | Size (LxWxH) mm | Unit price (USD)
IC Linear | 20 | 220V/60Hz | 0.5 | 2800 - 3000 | 140-150 | 3000 6500 |  | Samsung/ SSC | CE | Plastic G13 | 20,000 | 600x60x50 | 

## Slide 14
18W Hybrid LED Tube (Full Glass)
Product Description
Hybrid LED Tube is made of glass, which does not bend and is non-flammable, and powder coated to ensure good heat transfer. This Hybrid LED Tube can replace any existing T8 fluorescent tube and is compatible with AC 220V/60Hz. The tube can be installed using the existing ballast or bypass mode.
Features:
Samsung LED chip
Lifespan: 50,000 hours
CCT: 5700K
Energy efficient design
Cost-saving
Mercury and Lead Free
Specifications:
Installation:
Driver Type | Wattage (W) | Voltage/ Frequency | PF | Lumen (lm) | Luminous Efficacy (lm/W) | CCT (K) | Beam angle | LED chip | Certification | Base Cap | Lifetime (hrs) | Size (LxWxH) mm | Unit price (USD)
IC Linear | 20 | 220V/60Hz | 0.5 | 2800 - 3000 | 140-150 | 3000 6500 |  | Samsung/ SSC | CE | Plastic G13 | 20,000 | 600x60x50 | 

## Slide 15
LED FISHING LIGHT
Features:
Passed EMI/EMC
Excellent Surface treatment and painting for anti-salt corrosion.
IP for anti-water, No UV
Strong for impact and violence, reducing CO2 emission
Cost-saving
Specifications:
Type | Wattage (W) | Voltage (V) | Lumen (lm) | Luminous Efficacy (lm/W) | CCT (K) | IP | Weight (kg) | Lifetime (hrs) | Material | Size (LxWxH) mm | Unit price (USD)
Fishing alluring light | 300 | 220VAC | 39000 | 130 | 4000 | 66 | 5.5 | 20,000 | AL 6063 Anodized, Inox SUS 304 | 350x220x78 | 
Under water light | 600 | 220VAC | 48000 | 80 | 4000 | 68 | 4.0 | 20,000 | AL 6063 Strongly Anodized, PPMA, Inox SUS 304 | Φ102x450 | 
Under water light | 600 | 220VAC | 48000 | 80 | Green | 68 | 4.0 | 20,000 | AL 6063 Strongly Anodized, PPMA, Inox SUS 304 | Φ102x450 | 
Under water light | 200 | 220VAC | 17000 | 85 | 4000 | 68 | 3.0 | 20,000 | AL 6063 Strongly Anodized, PPMA, Inox SUS 304 | Φ102x440 | 
Under water light | 200 | 220VAC | 17000 | 85 | Green | 68 | 3.0 | 20,000 | AL 6063 Strongly Anodized, PPMA, Inox SUS 304 | Φ102x440 | 
Fishing alluring light
Under water light
Applications:

## Slide 16
THANK YOU!
Website: rangdong.com.vn
Telephone: (+84) 24 38 584 310 / 38 584 165
Email: export@rangdong.com.vn